## Slide 1: Open RAN (ORAN) and AI-Driven Networks
Module 5 – Week 5

## Slide 2: Introduction to Open and Intelligent Networks
- Shift from traditional vendor-locked RAN to open, flexible, and interoperable solutions
- ORAN enables multi-vendor ecosystems and AI-driven network intelligence
- Focus on automation, efficiency, and cost-effectiveness
- Supports 5G, 6G, and beyond evolution

## Slide 3: Traditional RAN vs Open RAN
**Traditional RAN:**
- Proprietary hardware + software
- Vendor lock-in
- Limited flexibility
- Slow innovation cycle
**Open RAN:**
- Open interfaces, disaggregated hardware/software
- Vendor interoperability
- Scalable and cost-effective
- Encourages ecosystem competition

## Slide 4: Open RAN Architecture Components
- RU (Radio Unit): Handles RF processing
- DU (Distributed Unit): Manages real-time baseband functions
- CU (Centralized Unit): Handles non-real-time baseband functions
- RIC (RAN Intelligent Controller): Optimizes and automates RAN functions
- Service Management and Orchestration (SMO): Coordinates multiple RAN functions

## Slide 5: RAN Intelligent Controller (RIC)
- Non-RT RIC (>1s): Policy control, analytics, AI/ML model training, long-term planning
- Near-RT RIC (10ms–1s): Dynamic optimization of radio resources, executes xApps, enables real-time traffic steering

## Slide 6: Open Interfaces
- F1: Between CU and DU
- E1: Between CU-CP and CU-UP
- A1: Between Non-RT RIC and Near-RT RIC
- E2: Between Near-RT RIC and CU/DU
- O1: For management and orchestration
Benefits:
- Vendor-neutral deployments
- Faster innovation
- AI/ML integration across multiple layers

## Slide 7: AI/ML Applications in RAN Optimization
- Intelligent radio resource management
- Dynamic spectrum allocation
- Energy efficiency optimization
- Traffic prediction and load balancing
- Anomaly detection and intrusion detection

## Slide 8: Self-Organizing Networks (SON)
- Self-configuration: Automated node deployment
- Self-optimization: Dynamic tuning of network parameters
- Self-healing: Automatic detection and correction of failures
- Self-protection: Defense against cyberattacks

## Slide 9: Predictive Maintenance with AI
- Anticipate hardware/software failures with AI/ML
- Proactive replacement of network elements
- Reduces downtime and improves QoS
- Based on vibration analysis, temperature monitoring, traffic anomalies

## Slide 10: Future of Open and Intelligent Networks
- 6G readiness with native AI integration
- Network slicing for customized services
- Edge computing integration with Open RAN
- Collaboration between operators, cloud providers, AI vendors
- Greater emphasis on cybersecurity and resilience

## Slide 11: Hands-On Lab Overview
Lab Activity:
1. Explore O-RAN Alliance documentation
2. Implement basic RAN optimization algorithms using Python
- Resource allocation simulation
- Load balancing using ML
3. Extend to anomaly detection using ML models

## Slide 12: Python Example – Resource Allocation
```python
import numpy as np
# Simulated resource allocation
users = 10
resources = 100
allocation = np.random.randint(1, 10, size=users)
allocation = allocation / sum(allocation) * resources
print("Resource Allocation per User:", allocation)
```

## Slide 13: Python Example – Traffic Prediction
```python
from sklearn.linear_model import LinearRegression
import numpy as np
# Simulated traffic data
X = np.array(range(1, 11)).reshape(-1, 1)
y = np.array([100,120,150,170,200,230,260,290,320,350])
model = LinearRegression().fit(X, y)
future = np.array([[11],[12],[13]])
print("Predicted Traffic:", model.predict(future))
```

## Slide 14: Summary
- Open RAN = disaggregated, interoperable, and intelligent
- RIC enables AI-driven real-time and non-real-time optimization
- AI/ML improves efficiency, resource utilization, and reliability
- SON and predictive maintenance enhance resilience
- Hands-on labs provide practical exposure to ORAN concepts

## Slide 15: References
- O-RAN Alliance (https://www.o-ran.org)
- 3GPP Specifications
- Industry reports on Open RAN and AI-driven networking
- Research papers on SON and AI-based predictive maintenance